# turnConveyor
A simple turning mechanism for Intralogistics

Here, the conveyor based turning will be developed in steps. A MVP product which can turn based on dynamics will be developed as an initial step. This will be broken into following steps.

Step 1 - Interface defenition and model building:
Components:
- 3 Conveyors
  - Turn Process = 2
  - Transfer Process = 1
- Ultrasonic Sensors
  - Start Turn Conveyor
  - Start the Turn Process
  - Stop the Turn Process and Start the Transfer
- Test Package
  - 250 X 125 X 100 (mm)
- Mechanism to detect the Package turned angle
  - Here a conveyor dynamics based turn is detected.

Interface: User <-> VREP
DataType	Variable	Init Value
BOOL	bStartTurnConveyor
BOOL	bStartTurnProcess
BOOL	bStopTurnProcess
REAL	rTurnSpeed
REAL	rTransferSpeed

Tasks
1. Concept Validation with V-REP
  1. Simple Simulation
  2. Turn Process
  3. Turn Quality
2. ROS Interface Defenition
3. Control Logic from an external controller.

Concept Validation:
Simple Simulation:
 Here a simple model was built in Coppelia Sim Software. This model can turn a package.However, the orientation of the package cannot be determined. To determine the orientation of the package, the following ideas can be implemented.
Idea 1 - Simple orienation detection from dynamics data
Idea 2 - Orientation detection using camera.

 Idea 1 :
We have the following data available for every turn process.
Package data => 250 X 125 X 100 mm.
Here, since both conveyors are moved with same speed in opposite direction, for a package of “x mm “ to be turned, it would require the package to travel “x/2” mm on the conveyor.

Hence, by tracking the conveyor distance, we can assume at a distance of “x/2” mm after synchronization, the package should be turned.